## Slide 1
Pico W
Sensor Kit
Component Guide
KV Bootcamp 2026 | 9–12 Jun 2026 | Hotel Granada, Johor Bahru
Raspberry Pi Pico W
DHT22 Temp+Humidity
MCP9700 Analog Temp
LDR Light Sensor

## Slide 2
What Each Component Does
Raspberry Pi Pico
USB Type-C Cable
HC-SR04 Ultrasonic
DHT22 Sensor
PIR Motion Sensor
Push Button
Temperature Sensor
LDR Sensor
Transistor (NPN)
Jumper Wires
DS1307 RTC I2C Module
LCD Display
LED
Buzzer
Resistor
Breadboard
SD Card Module

## Slide 3
OVERVIEW
What Each Component Does
Every kit streams one CSV row per second — feeding your pandas and ML exercises
Component
Measures
Pico W Pin
CSV Column
Raspberry Pi Pico W
Microcontroller + WiFi + on-board temp
—
onboard_temp_c
MCP9700 (Analog)
Ambient temperature (analog voltage)
A0 (GP26)
mcp_temp_c
LDR + 10kΩ Divider
Light level (raw ADC value 0–65535)
A1 (GP27)
ldr_raw
DHT22
Temperature + Relative Humidity (%)
GP15
dht_temp_c
dht_humidity_pct
All sensors powered from Pico W 3V3 OUT (pin 36). One CSV row per second over USB Serial and MQTT to broker seaicthree.local:1883

## Slide 4
PICO W
Raspberry Pi Pico W
The brain of the kit — RP2040 microcontroller with built-in WiFi
Processor
RP2040 dual-core ARM Cortex-M0+ 133 MHz
Memory
264 kB SRAM | 2 MB Flash
WiFi
CYW43439 — 2.4 GHz 802.11n
ADC
3× 12-bit ADC (GP26/27/28)
GPIO
26 multi-function GPIO pins
Power
3V3 OUT (pin 36) → sensors
Key Pins Used in This Kit
GP26 (A0)
MCP9700 analog output
GP27 (A1)
LDR voltage divider midpoint
GP15
DHT22 digital data
3V3 OUT
Power for all sensors (pin 36)

## Slide 5
DHT22
DHT22 — Temperature & Humidity Sensor
Digital sensor outputting calibrated temperature + relative humidity in one data packet
How It Works
Uses a capacitive humidity sensing element that changes electrical resistance with moisture.
Internal NTC thermistor measures temperature simultaneously.
Onboard ADC converts both readings to digital, sends via single-wire protocol.
Python reads with adafruit_dht library — one call returns both values.
Specifications
Temp Range
-40°C to +80°C
Accuracy
±0.5°C
Humidity
0–100% RH
Accuracy
±2–5% RH
Voltage
3.3V – 5V
Sample Rate
0.5 Hz (2s min)
Data Pin
GP15
Pull-up
4.7kΩ to 3V3 required
Connection
VCC → 3V3 | GND → GND | DATA → GP15 | 4.7kΩ pull-up on DATA

## Slide 6
MCP9700
MCP9700 — Analog Temperature Sensor
Linear active thermistor — outputs a voltage proportional to temperature. Simple and reliable.
The Formula:
Vout = 500mV + (Temp × 10mV/°C)
At 0°C → 0.500V At 25°C → 0.750V At 50°C → 1.000V
Reading in CircuitPython:
import analogio, board
adc = analogio.AnalogIn(board.A0)
voltage = adc.value * 3.3 / 65535
temp_c = (voltage - 0.5) / 0.01
Specifications
Range
-40°C to +150°C
Sensitivity
10 mV/°C
Package
TO-92 (3 pins)
Supply
2.3V – 5.5V
Pico Pin
A0 (GP26)
Output
Analog voltage
Connection
VDD → 3V3 | GND → GND | Vout → GP26 (A0) | No resistor needed

## Slide 7
LDR
LDR — Light Dependent Resistor
Photoresistor that changes resistance based on light intensity — used with voltage divider circuit
Voltage Divider Circuit:
3V3 ── LDR ──┬── 10kΩ ── GND
└── GP27 (A1)
ADC reads voltage at midpoint → converts to 0–65535 (12-bit ADC)
How Light Affects the Reading
Condition
LDR Resistance
Vout
ldr_raw value
Bright light
Low (~1kΩ)
High (~3V)
~60000+
Dim light
Medium (~10kΩ)
~1.65V
~32000
Dark / covered
High (~1MΩ)
Low (~0V)
~0–500
Connection
One LDR leg → 3V3 | Other LDR leg → midpoint → GP27 | 10kΩ from midpoint → GND

## Slide 8
WIRING
Complete Wiring Diagram
Power everything from 3V3 OUT (pin 36). Double-check polarity before plugging in USB.

## Slide 9
WIRING
Complete Wiring Diagram
Power everything from 3V3 OUT (pin 36). Double-check polarity before plugging in USB.

## Slide 10
PINOUT
Quick Pinout Reference
Component
Component Pin
Pico W Pin
Notes
MCP9700
VCC
3V3 OUT (pin 36)
3.3V supply
MCP9700
OUT
GP26 / A0 (pin 31)
10 mV/°C, 500 mV @ 0°C
MCP9700
GND
GND (any)
Common ground
LDR
VCC
3V3 OUT (pin 36)
Pull-up end
LDR
A0
GP27 / A1 (pin 32)
Voltage divider output
LDR
GND
GND (any)
Common ground
DHT22
+
3V3 OUT (pin 36)
3.3V supply
DHT22
OUT
GP15 (pin 20)
4.7kΩ pull-up to 3V3
DHT22
-
GND (any)
Common ground
All VCC/3V3 connections share pin 36. All GND connections can use any GND pin (3, 8, 13, 18, 23, 38).

## Slide 11
OUTPUT
CSV Output → pandas DataFrame
The device streams one CSV row per second
timestamp_ms
Pico W — Milliseconds since boot
onboard_temp_c
RP2040 — Chip internal temperature
mcp_temp_c
MCP9700 — Ambient temperature (GP26)
dht_temp_c
DHT22 — Air temperature (GP15)
dht_humidity_pct
DHT22 — Relative humidity % (GP15)
ldr_raw
LDR — Light ADC value 0–65535 (GP27)
comfort_level
Derived — Computed: comfortable / warm / hot
Load into pandas: df = pd.read_csv('sample_pico_readings.csv')

## Slide 12
FLOW
From Sensor to AI
The full data journey — from physical world to machine learning prediction
1
Physical World
Temperature, humidity, light — real environment in the room
2
Pico W Kit
MCP9700, DHT22, LDR read values → one CSV row per second
3
USB / MQTT
Data streams to laptop (USB Serial) and room broker (MQTT)
4
pandas (Day 2)
df = pd.read_csv(...) → clean, filter, groupby, visualize
5
ML Model (Day 3)
scikit-learn → train classifier → predict comfort_level
Make sure each kit streams a steady CSV

## Slide 13
TROUBLE
Troubleshooting Guide
Check these first before spending time debugging code
No CIRCUITPY drive
Re-flash. Confirm a data USB cable — not a charge-only cable.
dht_temp_c blank every row
DHT22 wiring or missing 4.7kΩ pull-up. Re-seat data wire on GP15. Occasional blank row is normal.
mcp_temp_c wildly wrong
Check MCP9700 orientation. Confirm Vout is on GP26, not a power pin. Flat side faces you when reading label.
ldr_raw stuck at 0 or 65535
Voltage divider not wired correctly. Check 10kΩ pulldown to GND and the A1 (GP27) connection.
ImportError: adafruit_dht
Library missing from CIRCUITPY/lib/. Redo Step 2 — copy adafruit_dht.mpy to lib/.
No '# wifi ok' line
Wrong SSID/password in secrets.py, or you flashed the plain Pico build instead of Pico W build.
No '# mqtt connected' but WiFi ok
Broker unreachable. Device still streams over USB — acceptable for the lab exercises.